## Slide 1: CIS 185 CCNP ROUTE Chapter 3: Implementing OSPF Part 1
Rick Graziani
Cabrillo College
graziani@cabrillo.edu
2017

## Slide 2: Basic OSPF

## Slide 3: Types of Routing Protocols
* OSPFv3 supports routing both IPv4 and IPv6.
Distance Vector Routing Protocols |  | Link State Routing Protocols |  | Path Vector
RIPv2 | EIGRP | OSPFv2 | IS-IS | BGP-4
RIPng | EIGRP for IPv6 | OSPFv3 * | IS-IS for IPv6 | BGP-4 for IPv6 or MP-BGP
Distance Vector
Link State
Path Vector
Interior Gateway Protocols
Exterior Gateway Protocols
IPv4
IPv6

## Slide 4: Link State Concepts
Link states - Information about the state of a router’s links
This information includes interface’s:
  IP address/mask
  Type of network
    Ethernet (broadcast) or serial point-to-point link
  Cost of that link
  Any neighbor routers on that link
Link 2
Network: 10.2.0.0/16
IP address: 10.2.0.1
Type of network: Serial
Cost of that link: 20
Neighbors: R2
Link 3
Network: 10.3.0.0/16
IP address: 10.3.0.1
Type of network: Serial
Cost of that link: 5
Neighbors: R3
Link 4
Network: 10.4.0.0/16
IP address: 10.4.0.1
Type of network: Serial
Cost of that link: 20
Neighbors: R4
Link 1
Network: 10.1.0.0/16
IP address: 10.1.0.1
Type of network: Ethernet
Cost of that link: 2
Neighbors: None
Notes: A link is an interface on a router.
For the link participate in the link-state routing process, it must be:
  In the up state.
  Included in one of the network statements.

## Slide 5: Link State Concepts

## Slide 6: R1 Processes the LSPs from R2
The SPF algorithm begins by processing the following LSP information from R2:
  Connected to neighbor R1 on network 10.2.0.0/16, cost of 20
  Connected to neighbor R5 on network 10.9.0.0/16, cost of 10
  Has a network 10.5.0.0/16, cost of 2
Red: New information for tree.
Notes: The SPF algorithm begins by processing the following LSP information from R2:
  Connected to neighbor R1 on network 10.2.0.0/16, cost of 20
  Connected to neighbor R5 on network 10.9.0.0/16, cost of 10
  Has a network 10.5.0.0/16, cost of 2

## Slide 7: SPF Tree
R1 has now constructed the complete SPF tree.
Notes: R1 has now constructed the complete SPF tree.

## Slide 8
20
2
Determining the Shortest Path
Network 10.5.0.0/16 via R2 Serial 0/0/0 at a cost of 22

## Slide 9: Generating a Routing Table from the SPF Tree
These paths listed previously can now be added to the routing table.
The routing table will also include
  Directly connected networks
  Routes from any other sources, such as static routes.
Packets will now be forwarded according to these entries in the routing table.
SPF Tree for R1
Notes: These paths listed previously can now be added to the routing table.
The routing table will also include
  Directly connected networks
  Routes from any other sources, such as static routes.
Packets will now be forwarded according to these entries in the routing table.

## Slide 10
OSPF packet types

## Slide 11
Hello 10.6.0.1
Hello 10.5.0.1
Hello 10.6.0.1 10.5.0.1
Hello 10.5.0.1 10.6.0.1
Down
Init
Down
Init
2-way
2-way
Down State - Init State – Two Way State
Down State - OSPF routers send Hello packets at regular intervals (10 sec.) to establish neighbors.
When a router (sends or) receives its first Hello packet, it enters the init state.
  Hello packet contains a list of known neighbors.
When the router sends a Hello packet (unicast reply) to the neighbor with its RouterID and the neighbor sends a Hello packet packet back with that Router ID, the router’s interface will transition to the two-way state.
Now, the router is ready to take the relationship to the next level.
Establishing Adjacencies

## Slide 13
OSPF packet types
Partial list: More later!

## Slide 14: Basic OSPF Configuration

## Slide 15: OSPF Reference Topology
Notes: Media Description:
Create the media as indicated.

## Slide 16: Neighbor Establishment, OSPF Hello and Dead Intervals
Before an OSPF router can flood its link states, must discover neighbors.
Before two routers can form an OSPF neighbor adjacency, they must agree on three values:
  Hello interval
  Dead interval
  Network type
  MTU
Both the interfaces must be part of the same network, including having the same subnet mask.
More later
Hello, I’m R1
Hello, I’m R2
Hello, I’m R3
Notes: Before an OSPF router can flood its link states, must discover neighbors.
Receipt confirms there is another OSPF router on this link.
Adjacency is now established.
Routers are not considered fully adjacent, at this point each router is aware of the other OSPF router on the link.
Before two routers can form an OSPF neighbor adjacency, they must agree on three values:
  Hello interval
  Dead interval
  Network type
Both the interfaces must be part of the same network, including having the same subnet mask.

## Slide 17: Hello Intervals
By default, OSPF Hello packets are sent:
  10 seconds on multiaccess and point-to-point segments
  30 seconds on nonbroadcast multiaccess (NBMA) segments (Frame Relay, X.25, ATM).
Sent to ALLSPFRouters at 224.0.0.5
Hello, I’m R1
Hello, I’m R2
Hello, I’m R3
Notes: By default, OSPF Hello packets are sent:
  10 seconds on multiaccess and point-to-point segments
  30 seconds on nonbroadcast multiaccess (NBMA) segments (Frame Relay, X.25, ATM).
In most cases, OSPF Hello packets are sent as multicast to an address reserved for ALLSPFRouters at 224.0.0.5.

## Slide 18: Dead Intervals
Dead interval - Period, expressed in seconds, that the router will wait to receive a Hello packet before declaring the neighbor “down.”
Cisco uses a default of four times the Hello interval.
  40 seconds - Multiaccess and point-to-point segments.
  120 seconds - NBMA networks.
Dead interval expires
  OSPF removes that neighbor from its link-state database.
  Floods the link-state information about the “down” neighbor out all OSPF-enabled interfaces.
Hello, I’m R1
Hello, I’m R2
Hello, I’m R3
Notes: Dead interval - Period, expressed in seconds, that the router will wait to receive a Hello packet before declaring the neighbor “down.”
Cisco uses a default of four times the Hello interval.
  40 seconds - Multiaccess and point-to-point segments.
  120 seconds - NBMA networks.
Dead interval expires
  OSPF removes that neighbor from its link-state database.
  Floods the link-state information about the “down” neighbor out all OSPF-enabled interfaces.
Network types are discussed later in the chapter.

## Slide 19: The router ospf Command
The process-id
  Between 1 and 65,535
  Chosen by the network administrator.
Locally significant:
  Does not have to match other OSPF routers.
  This differs from EIGRP.
We are using the same process ID simply for consistency.
R1(config)# router ospf 10
R1(config-router)#
Notes: The process-id
  Between 1 and 65,535
  Chosen by the network administrator.
Locally significant:
  Does not have to match other OSPF routers.
  This differs from EIGRP.
We are using the same process ID simply for consistency.

## Slide 20: OSPF Router ID
A router is known to OSPF by the OSPF router ID number.
  LSDBs use the OSPF router ID to differentiate one router from the next.
By default, the router ID is the highest IP address on an active interface at the moment of OSPF process startup.
However, for stability reason, it is recommended that the router-id command or a loopback interface be configured.
Notes: The OSPF database uses the OSPF router ID to uniquely describe each router in the network. Remember that every router keeps a complete topology database of all routers and links in an area (or network); therefore each router should have a unique router ID.
As a review, remember that the router ID is a unique IP address that can be assigned in the following ways:
  By default, the highest IP address of any active physical interface when OSPF starts is chosen as the router ID. The interface does not have to be part of the OSPF process, but it has to be up. There must be at least one up IP interface on the router for OSPF to use as router ID. If no up interface with an IP address is available when the OSPF process starts, the “OSPF process cannot start” message occurs
  If there is a loopback interface, its address will always be preferred as the router ID instead of a physical interface address, because a loopback interface never goes down. If there is more than one loopback interface, then the highest IP address on any active loopback interface becomes the router ID.
  Finally, you can use the router-id command to set the router ID. This is the preferred way to establish a router ID and should always used in preference to the other two procedures.
Once the OSPF router ID is set, it does not change, even if the interface that the router is using for the router ID goes down. The OSPF router ID changes only if the router reloads or if the OSPF routing process restarts.
If no interface is up when the OSPF process starts, you will get the following error message: p5r2(config)#router ospf 1
  2w1d: %OSPF-4-NORTRID: OSPF process 1 cannot start.

## Slide 21
Cisco routers derive the router ID based on three criteria and with the following precedence:
  1. IP address configured with the OSPF router-id command.
  2. Highest IP address of any of its loopback interfaces.
  3. Highest active IP address of any of its physical interfaces.
    The interface does not need to be enabled for OSPF, i.e. it does not need to be included in one of the OSPF network commands.
OSPF Router ID
What’s my Router ID?
What’s my Router ID?
What’s my Router ID?
Notes: Cisco routers derive the router ID based on three criteria and with the following precedence:
  1. Use the IP address configured with the OSPF router-id command.
  2. If the router ID is not configured, the router chooses the highest IP address of any of its loopback interfaces.
  3. If no loopback interfaces are configured, the router chooses the highest active IP address of any of its physical interfaces.
    The interface does not need to be enabled for OSPF, i.e. it does not need to be included in one of the OSPF network commands.

## Slide 22: Define the Router ID
Assign a specific router ID to the router.
Router(config)# router ospf process-id
Router(config-router)# router-id ip-address
Any unique arbitrary 32-bit value in an IP address format (dotted decimal) can be used.
  If this command is used on an OSPF process that is already active, then the new router ID takes effect:
    After the next router reload.
    After a manual restarting of the OSPF process using the clear ip ospf process privileged EXEC command.
Router# clear ip ospf process
Notes: Use the OSPF router-id command to ensure that OSPF selects a specific router ID. The ip-address parameter can be any unique arbitrary 32-bit value in an IP address dotted decimal format.
After the router-id command is configured, use the clear ip ospf process command. This command restarts the OSPF routing process so that it will reselect the new IP address as its router ID.

## Slide 23: Define the Router ID
R1(config)# router ospf 10
R1(config-router)# router-id 1.1.1.1
R1(config-router)# end
R1#
*Mar 25 19:50:36.595: %SYS-5-CONFIG_I: Configured from console by console
R1#

## Slide 24: Define the Router ID
R1# show ip protocols
*** IP Routing is NSF aware ***
Routing Protocol is "ospf 10"
Outgoing update filter list for all interfaces is not set
Incoming update filter list for all interfaces is not set
Router ID 1.1.1.1
Number of areas in this router is 0. 0 normal 0 stub 0 nssa
Maximum path: 4
<Output omitted>

## Slide 25: Changing the OSPF Router-ID
R1(config)# router ospf 10
R1(config-router)# router-id 1.1.1.1
% OSPF: Reload or use "clear ip ospf process" command, for this to take effect
R1(config-router)# end
R1#
R1# clear ip ospf process
Reset ALL OSPF processes? [no]: y
R1#
*Mar 25 19:46:22.423: %OSPF-5-ADJCHG: Process 10, Nbr 3.3.3.3 on Serial0/0/1 from FULL to DOWN, Neighbor Down: Interface down or detached
*Mar 25 19:46:22.423: %OSPF-5-ADJCHG: Process 10, Nbr 2.2.2.2 on Serial0/0/0 from FULL to DOWN, Neighbor Down: Interface down or detached
*Mar 25 19:46:22.475: %OSPF-5-ADJCHG: Process 10, Nbr 3.3.3.3 on Serial0/0/1 from LOADING to FULL, Loading Done
*Mar 25 19:46:22.475: %OSPF-5-ADJCHG: Process 10, Nbr 2.2.2.2 on Serial0/0/0 from LOADING to FULL, Loading Done
R1#
R1# show ip protocols | section Router ID
Router ID 1.1.1.1
R1#

## Slide 26: The network Command
The network command (same function as when used with other IGP routing protocols)
  Any interfaces on a router that match the network address in the network command will be enabled to send and receive OSPF packets.
  This network (or subnet) will be included in OSPF routing updates.
Requires the wildcard mask.
  Used to specify the interface or range of interfaces that will be enabled for OSPF.
Router(config-router)# network network-address wildcard-mask area area-id
Notes: The network command (same function as when used with other IGP routing protocols):
  Any interfaces on a router that match the network address in the network command will be enabled to send and receive OSPF packets.
  This network (or subnet) will be included in OSPF routing updates.
Requires the wildcard mask.
Used to specify the interface or range of interfaces that will be enabled for OSPF.

## Slide 27: The network Command
The wildcard mask can be configured as the inverse of a subnet mask.
Note:
  Like EIGRP, some Cisco IOS software versions allow you to simply enter the subnet mask instead of the wildcard mask.
  The Cisco IOS software then converts the subnet mask to the wildcard mask format.
255.255.255.255
- 255.255.255.240 Subtract the subnet mask
---------------
0. 0. 0. 15 Wildcard mask
Router(config-router)# network network-address wildcard-mask area area-id
Notes: The wildcard mask can be configured as the inverse of a subnet mask.
R1’s FastEthernet 0/0 interface is on the 172.16.1.16/28 network.
The subnet mask for this interface is /28 or 255.255.255.240
The wildcard mask would be 0.0.0.15.
Note:
  Like EIGRP, some Cisco IOS software versions allow you to simply enter the subnet mask instead of the wildcard mask.
  The Cisco IOS software then converts the subnet mask to the wildcard mask format.

## Slide 28: The network Command
The area area-id refers to the OSPF area.
A group of routers that share link-state information.
  Identical link-state databases.
In this chapter, we configure all the OSPF routers within a single area.
  This is known as single-area OSPF.
The network commands must be configured with the same area ID on all routers.
  Good practice to use an area ID of 0 with single-area OSPF.
Router(config-router)# network network-address wildcard-mask area area-id
Notes: The area area-id refers to the OSPF area.
  A group of OSPF routers that share link-state information.
  All OSPF routers in the same area must have the same link-state information in their link-state databases.
  This is accomplished by routers flooding their individual link states to all other routers in the area.
In this chapter, we configure all the OSPF routers within a single area.
  This is known as single-area OSPF.
The network commands must be configured with the same area ID on all routers.
Although any area ID can be used, it is good practice to use an area ID of 0 with single-area OSPF.
This convention makes it easier if the network is later configured as multiple OSPF areas where area 0 becomes the backbone area.
  Mult-Area OSPF is discussed in CCNP.

## Slide 29: Advertising OSPF Networks
R1(config)# router ospf 10
R1(config-router)# router-id 1.1.1.1
R1(config-router)# network 172.16.1.0 0.0.0.255 area 0
R1(config-router)# network 172.16.3.0 0.0.0.3 area 0
R1(config-router)# network 192.168.10.4 0.0.0.3 area 0
R1(config-router)# end
R1#

## Slide 30: Optional Method: Identify OSPF Networks
R1(config)# interface gig 0/0
R1(config-router)# ip ospf 10 area 0
R1(config-router)# exit
R1(config)# interface serial 0/0/0
R1(config-router)# ip ospf 10 area 0
R1(config-router)# exit
R1(config)# interface serial 0/0/1
R1(config-router)# ip ospf 10 area 0
R1(config-router)# end
No network command needed.
Because this command is configured explicitly for the interface, it takes precedence over the network area command.

## Slide 31: Fine Tuning OSPF Interfaces

## Slide 32: Modifying OSPF Intervals
It might be desirable to change the OSPF timers so that routers will detect network failures in less time.
Before changing any timer default values, be sure to give it careful consideration and understand the effects of making those changes.
The OSPF Hello and Dead intervals are configurable on a per-interface basis.
NOTE:
  OSPF intervals must match or a neighbor adjacency does not occur.
  EIGRP hello and hold timers do NOT have to match.
Router(config-if)# ip ospf hello-interval seconds
Router(config-if)# ip ospf dead-interval seconds
Notes: It might be desirable to change the OSPF timers so that routers will detect network failures in less time.
Before changing any timer default values, be sure to give it careful consideration and understand the effects of making those changes.

## Slide 33: Verifying the OSPF Intervals on R1
R1# show ip ospf interface serial 0/0/0
Serial0/0/0 is up, line protocol is up
Internet Address 172.16.3.1/30, Area 0, Attached via Network Statement
Process ID 10, Router ID 1.1.1.1, Network Type POINT_TO_POINT, Cost: 64
Topology-MTID Cost Disabled Shutdown Topology Name
0 64 no no Base
Transmit Delay is 1 sec, State POINT_TO_POINT
Timer intervals configured, Hello 10, Dead 40, Wait 40, Retransmit 5
oob-resync timeout 40
Hello due in 00:00:03
<Output omitted>
R1#
Notes: Media Description:
Create the media as indicated.

## Slide 34: Changing the OSPF Intervals on R1
R1(config)# interface Serial 0/0/0
R1(config-if)# ip ospf hello-interval 5
R1(config-if)# ip ospf dead-interval 20
R1(config-if)# end
R1#
*Apr 7 17:28:21.529: %OSPF-5-ADJCHG: Process 10, Nbr 2.2.2.2 on Serial0/0/0 from FULL to DOWN, Neighbor Down: Dead timer expired
R1# show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
3.3.3.3 0 FULL/ - 00:00:37 192.168.10.6 Serial0/0/1
R1#
Hello = 5 sec Dead = 20 sec
Hello = 10 sec Dead = 40 sec
Remember, OSPF Hello and Dead intervals must be equivalent between neighbors.
Loss of adjacency with R2 but R3 is still a neighbor.

## Slide 35: Changing the OSPF Intervals on R2
R2(config)# interface serial 0/0/0
R2(config-if)# ip ospf hello-interval 5
R2(config-if)#
*Apr 7 17:41:49.001: %OSPF-5-ADJCHG: Process 10, Nbr 1.1.1.1 on Serial0/0/0 from LOADING to FULL, Loading Done
R2(config-if)# end
R2#
R2# show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
3.3.3.3 0 FULL/ - 00:00:35 192.168.10.10 Serial0/0/1
1.1.1.1 0 FULL/ - 00:00:17 172.16.3.1 Serial0/0/0
R2#
Hello = 5 sec Dead = 20 sec
Hello = 5 sec Dead = 20 sec
OSPF automatically adjusts Dead timer to 4 times the Hello timer.

## Slide 36: Passive Interfaces

## Slide 37: Passive Interface
By default, OSPF messages are forwarded out all OSPF-enabled interfaces.
Notes:   Inefficient Use of Bandwidth - Available bandwidth is consumed transporting unnecessary messages. Messages are multicasted; therefore, switches are also forwarding the messages out all ports.
  Inefficient Use of Resources - All devices on the LAN must process the message and eventually discard the message.
Increased Security Risk - Advertising updates on a broadcast network is a security risk. OSPF messages can be intercepted with packet sniffing software. Routing updates can be modified and sent back to the router, corrupting the routing table with false metrics that misdirect traffic.

## Slide 38: Configuring Passive Interfaces on R1 & R2
R1(config)# router ospf 10
R1(config-router)# passive-interface GigabitEthernet 0/0
R1(config-router)# end
R1#
R2(config)# router ospf 10
R2(config-router)# passive-interface GigabitEthernet 0/0
R2(config-router)# end
R2#

## Slide 39: Verifying Passive Interfaces on R1 and R2
R1# show ip protocols | section Passive
Passive Interface(s):
GigabitEthernet0/0
R1#
R2# show ip protocols | section Passive
Passive Interface(s):
GigabitEthernet0/0
R2#

## Slide 40: Configuring Passive Interfaces on R3
R3(config)# router ospf 10
R3(config-router)# passive-interface default
R3(config-router)#
*Apr 7 16:22:58.090: %OSPF-5-ADJCHG: Process 10, Nbr 1.1.1.1 on Serial0/0/0 from FULL to DOWN, Neighbor Down: Interface down or detached
*Apr 7 16:22:58.090: %OSPF-5-ADJCHG: Process 10, Nbr 2.2.2.2 on Serial0/0/1 from FULL to DOWN, Neighbor Down: Interface down or detached
R3(config-router)#
R3(config-router)# no passive-interface serial 0/0/0
*Apr 7 16:23:18.590: %OSPF-5-ADJCHG: Process 10, Nbr 1.1.1.1 on Serial0/0/0 from LOADING to FULL, Loading Done
R3(config-router)#
R3(config-router)# no passive-interface serial 0/0/1
R3(config-router)#
*Apr 7 16:23:24.462: %OSPF-5-ADJCHG: Process 10, Nbr 2.2.2.2 on Serial0/0/1 from LOADING to FULL, Loading Done

## Slide 41: DR/BDR Multiaccess Networks

## Slide 42
Solution: Designated Router
OSPF elects a Designated Router (DR) to be the collection and distribution point for LSAs sent and received.
A Backup Designated Router (BDR) is also elected in case the DR fails.
All other routers become DROthers.

## Slide 43
DROthers only form full adjacencies with the DR and BDR in the network.
  send their LSAs to the DR and BDR, multicast address 224.0.0.6 (ALLDRouters)
R1 sends LSAs to the DR (The BDR listens, too.)
The DR is responsible for forwarding the LSAs from R1 to all other routers.
  DR uses the multicast address 224.0.0.5 (AllSPFRouters, all OSPF routers).
  Only one router doing all the flooding.
DROther
DROther
DROther
DROther
DROther
DROther
224.0.0.6
224.0.0.5

## Slide 44
DR/BDR Election
The following criteria are applied:
  1. DR: Router with the highest OSPF interface priority.
  2. BDR: Router with the second highest OSPF interface priority.
  3. If OSPF interface priorities are equal, the highest router ID is used to break the tie.
Default OSPF interface priority is 1.
Current configuration, the OSPF router ID is used to elect the DR and BDR.
DR
BDR
DROther

## Slide 45
RouterA# show ip ospf interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
Internet Address 192.168.1.1/24, Area 0
Process ID 1, Router ID 192.168.31.11, Network Type BROADCAST, Cost: 1
Transmit Delay is 1 sec, State DROTHER, Priority 1
Designated Router (ID) 192.168.31.33, Interface address 192.168.1.3
Backup Designated router (ID) 192.168.31.22, Interface address 192.168.1.2
Timer intervals configured, Hello 10, Dead 40, Wait 40, Retransmit 5
<output omitted>
Verifying Router States

## Slide 46
Control the election of these routers with the ip ospf priority interface command.
Priority (Highest priority wins):
  0 = Cannot become DR or BDR
  1 = Default
    Therefore, the router ID determines the DR and BDR.
Priorities are an interface-specific value, they provide better control of the OSPF multiaccess networks.
They also allow a router to be the DR in one network and a DROther in another.
Router(config-if)# ip ospf priority {0 - 255}

## Slide 47
OSPF Interface Priority
The OSPF interface priority can be viewed using the show ip ospf interface command.
RouterA# show ip ospf interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
Internet Address 192.168.1.1/24, Area 0
Process ID 1, Router ID 192.168.31.11, Network Type BROADCAST, Cost: 1
Transmit Delay is 1 sec, State DROTHER, Priority 1
Designated Router (ID) 192.168.31.33, Interface address 192.168.1.3
Backup Designated router (ID) 192.168.31.22, Interface address 192.168.1.2
Timer intervals configured, Hello 10, Dead 40, Wait 40, Retransmit 5
<output omitted>

## Slide 48
RouterA(config)# interface fastethernet 0/0
RouterA(config-if)# ip ospf priority 200
RouterB(config)# interface fastethernet 0/0
RouterB(config-if)# ip ospf priority 100
Pri = 200
Pri = 100
Highest priority wins
After doing a shutdown and a no shutdown on the Fast Ethernet 0/0 interfaces of all three routers, we see the result of the change of OSPF interface priorities.

## Slide 49
Clarifications regarding DR/BDR
Hello packets are still exchanged between all routers on a multi-access segment (DR, BDR, DROthers,….) to maintain neighbor adjacencies.
OSPF LSA packets (coming) are packets which are sent from the BDR/DROthers to the DR, and then from the DR to the BDR/DROthers. (The reason for a DR/BDR.)
Normal routing of IP packets still takes the lowest cost route, which might be between two DROthers.

## Slide 50: OSPF Metric (Cost)

## Slide 51: OSPF Metric
The OSPF metric is called cost. The following passage is from RFC 2328:
  A cost is associated with the output side of each router interface. This cost is configurable by the system administrator. The lower the cost, the more likely the interface is to be used to forward data traffic.
RFC 2328 does not specify which values should be used to determine the cost.
Notes: The OSPF metric is called cost. The following passage is from RFC 2328:
  A cost is associated with the output side of each router interface. This cost is configurable by the system administrator. The lower the cost, the more likely the interface is to be used to forward data traffic.
RFC 2328 does not specify which values should be used to determine the cost.

## Slide 52: OSPF Metric
Cisco IOS software uses the cumulative bandwidths of the outgoing interfaces from the router to the destination network as the cost value.
108 is known as the reference bandwidth
  So that interfaces with the higher bandwidth values will have a lower calculated cost.
Cisco IOS Cost for OSPF = 108/bandwidth in bps
Notes: Cisco IOS software uses the cumulative bandwidths of the outgoing interfaces from the router to the destination network as the cost value.
108 is known as the reference bandwidth
Dividing 108 by the interface bandwidth is done so that interfaces with the higher bandwidth values will have a lower calculated cost.
Remember, in routing metrics, the lowest-cost route is the preferred route.

## Slide 53: Accommodating 10Gig Interfaces
R1(config-router)# auto-cost reference-bandwidth 10000
In Mb/s

## Slide 54: Adjusting to Reference Bandwidth for Gig
R1(config)# router ospf 10
R1(config-router)# auto-cost reference-bandwidth 1000
R2(config)# router ospf 10
R2(config-router)# auto-cost reference-bandwidth 1000
R3(config)# router ospf 10
R3(config-router)# auto-cost reference-bandwidth 1000
Cost = 1
Cost = 647

## Slide 55: Modifying the Cost of the Link
Both sides of the link should be configured to have the same value.
R1(config)# inter serial 0/0/1
R2(config-if)# bandwidth 64
R2(config-if)# inter serial 0/0/1
R2(config-if)# bandwidth 1024
R3(config)# inter serial 0/0/1
R2(config-if)# bandwidth 1024
R3(config-if)# inter serial 0/0/0
R3(config-if)# bandwidth 64
Notes: Both sides of the link should be configured to have the same value.

## Slide 56: The ip ospf cost Command
An alternative method to using the bandwidth command is to use the ip ospf cost command, which allows you to directly specify the cost of an interface.
This will not change the output of the show ip ospf interface command.
R1(config)# interface serial 0/0/1
R1(config-if)# ip ospf cost 15625
R1(config)# inter serial 0/0/1
R1(config-if)# bandwidth 64
R1(config-if)# end
R1# show ip ospf interface serial 0/0/0
Serial0/0 is up, line protocol is up
Internet Address 192.168.10.1/30, Area 0
Process ID 1, Router ID 10.1.1.1, Network Type POINT_TO_POINT,Cost: 15625
1,000,000,000/64,000 = 15625
Notes: An alternative method to using the bandwidth command is to use the ip ospf cost command, which allows you to directly specify the cost of an interface.
This will not change the output of the show ip ospf interface command,

## Slide 57: IP MTU and OSPF

## Slide 58
IPv4 Fragmentation
IPv4 fields used for fragmentation and reassembly.
Intermediate devices such as IPv6 routers do not perform fragmentation.
Any fragmentation needed will be handled by the source using an extension header.
IPv4
IPv6

## Slide 59
Source
R1
R2
R3
PCB
MTU of outgoing link smaller than packet size – fragment IPv4 packet.
1
2
PCA
Destination
IPv4 Fragmentation
Link with smaller MTU
IPv4 Packet
IPv4 Packet
IPv4 Packet
IPv4 Packet
IPv4 Packet
It is my job to reassemble the packet fragments.
3
IPv4 Packet
IPv4 Packet
IPv4 Packet
IPv4 requires that every link have a minimum MTU of 68 bytes.
Every internet destination must be able to receive a packet of 576 bytes either in one piece or in fragments to be reassembled.
Notes: http://www.potaroo.net/ispcol/2009-01/mtu6.html
RFC791:
Every internet module must be able to forward a datagram of 68 octets without further fragmentation. This is because an internet header may be up to 60 octets, and the minimum fragment is 8 octets.
Every internet destination must be able to receive a datagram of 576 octets either in one piece or in fragments to be reassembled.

## Slide 60: IP MTU
OSPF relies on IPv4 for fragmentation.
IPv6 routers do not fragment packets – drops packet and returns ICMPv6 Packet Too Big message with MTU size to the source.
If MTUs are mismatched between two neighbors, this could introduce issues with exchange of link-state packets, resulting in continuous retransmissions.
OSPF requires that the same IPv4 MTU be configured on both sides of the link.
If neighbors have a mismatched IPv4 MTU configured, they will not be able to form full OSPF adjacency.
If necessary, the IP MTU can be changed on the interface.
Router(config)# interface fa 0/2
Router(config-if)# ip mtu 1400
Router(config-if)# ipv6 mtu 1400

## Slide 61: Multi-Area OSPF

## Slide 62: Multi-Area OSPF
Hierarchical routing enables you to separate large internetworks (autonomous systems) into smaller internetworks that are called areas.
With this technique, routing still occurs between the areas (called inter-area routing).
Some operations are restricted within an area:
  Flooding of LSAs
  Recalculating the database
  Re-running the SPF algorithm

## Slide 63: Multi-Area OSPF

## Slide 64: Multi-Area OSPF
Internal: Routers with all their interfaces within the same area
Backbone: Routers with at least one interface connected to area 0
ASBR: (Autonomous System Boundary Router): Routers that have at least one interface connected to an external internetwork (another autonomous system)
ABR: (Area Border Router): Routers with interfaces attached to multiple areas.

## Slide 65: Single Area OSPF
In single area OSPF, all routers are in area 0.
  Area 0 is also called the backbone area.
Single area OSPF is useful in smaller networks with few routers.
R2
OSPF Area 0
R1
Notes: Media Description:
Create the media as indicated.

## Slide 66: Issues With a Large OSPF Area
Large routing table:
  OSPF does not automatically summarize routes and therefore routing tables can become very large, depending on the size of the network.
R1
R2
My routing table is too big and I am running low on memory.
Notes: Media Description:
Create the media as indicated.

## Slide 67: Issues With a Large OSPF Area
Large link-state database (LSDB):
  The LSDB maintain an entry for every network in the area, even if not every route is selected for the routing table.
  Too many routers in one area would make the LSDBs very large and increase the load on the CPU.
R1
R2
I’m receiving too many LSAs.
Notes: Media Description:
Create the media as indicated.

## Slide 68: Issues With a Large OSPF Area
Frequent SPF algorithm calculations:
  In a large network, changes are inevitable, so the routers spend many CPU cycles recalculating the SPF algorithm and updating the routing table.
R1
R2
My SPF algorithm is running too often for me to route properly.
Notes: Media Description:
Create the media as indicated.

## Slide 69: Multi-Area OSPF
Multiarea OSPF uses a two-layer area hierarchy using a backbone area interconnecting regular areas.
  Useful in larger network deployments to reduce processing and memory overhead.
All regular areas must interconnect to the backbone area (area 0).
  Interconnecting routers are called Area Border Routers (ABR).
R1
R2
Area 1
Area 0
Area 51
Notes: Media Description:
Create the media as indicated.

## Slide 70: Backbone (Transit) Area
OSPF area whose primary function is the fast and efficient movement of IP packets.
  Backbone areas interconnect with other OSPF area types.
  Generally, end users are not found within a backbone area.
The backbone area is also called OSPF area 0.
  Hierarchical networking defines area 0 as the core to which all other areas directly connect.
R1
R2
Area 1
Area 0
Area 51
Notes: Media Description:
Create the media as indicated.

## Slide 71: Regular or Normal Areas
Connects users and resources.
  Areas are usually set up along functional or geographical groupings.
By default, all traffic from other areas must cross an ABR.
  A regular area does not allow traffic from another area to use its links to reach other areas.
R1
R2
Area 1
Area 0
Area 51
Notes: Media Description:
Create the media as indicated.

## Slide 72: Multiarea OSPF Advantages
Smaller routing tables:
  Fewer routing table entries because network addresses can be summarized between areas.
  Route summarization is not enabled by default.
Reduced link-state update overhead:
  Minimizes processing and memory requirements.
Reduced frequency of SPF calculations:
  Localizes the impact of a topology change within an area.
  For instance, it minimizes routing update impact because LSA flooding stops at the area boundary.
R1
R2
Area 1
Area 0
Area 51

## Slide 73: Topology Change Impacts Local Area Only
The ABR (R2) isolates the fault to area 51 only.
  Link failure affects the local area only (area 51)
Routers in areas 0 and 1 do not need the run the SPF algorithm.
Only R2 and routers in area 51 exchange LSAs and run the SPF algorithm.
R1
R2
Link fails
Area 1
Area 0
Area 51
Notes: Media Description:
Create the media as indicated.

## Slide 74: Cisco OSPF Implementation Guidelines
The optimal number of routers per area varies based on factors such as network stability.
However, Cisco guidelines recommend:
  A router should not be in more than three areas.
  An area should have no more than 50 routers.
  Any single router should not have more than 60 neighbors.
R1
R2
Area 1
Area 0
Area 51
Notes: Media Description:
Create the media as indicated.

## Slide 75: Internal Routers
This is a router that has all of its interfaces in the same area.
All internal routers in an area have identical LSDBs.
R1
R2
Internet
Area 1
Area 0
Area 51
Notes: Media Description:
Create the media as indicated.

## Slide 76: Backbone Routers
Backbone router have at least one interface in Area 0.
This is a router with an interface(s) in the backbone area.
R1
R2
Internet
Area 1
Area 0
Area 51
Notes: Media Description:
Create the media as indicated.

## Slide 77: Area Border Router (ABR)
This is a router that has interfaces attached to multiple areas.
ABRs:
  Maintain separate LSDBs for each area it is connected to.
  Are exit points for the area.
  Distribute the routing information into the backbone and the backbone routers then forward the information to the other ABRs.
R1
R2
Internet
Area 1
Area 0
Area 51
Notes: Media Description:
Create the media as indicated.

## Slide 78: Autonomous System Boundary Router (ASBR)
This is a router that has at least one interface attached to an external non-OSPF network.
An ASBR can redistribute non-OSPF network information into and out of the OSPF network.
R1
R2
Internet
Area 1
Area 0
Area 51
Notes: Media Description:
Create the media as indicated.

## Slide 79: Configuring Basic Multi-Area OSPF

## Slide 80: OSPF Multiarea OSPF Topology
G0/1 .1
.1 G0/0
Area 2
192.168.1.0/24
Area 0
R3
S0/0/1 .6
.1 S0/0/0
S0/0/1 .5
10.2.1.0/24
G0/0 .1
10.1.2.0/24
192.168.10.0/30
192.168.10.4/30
.2 S0/0/0
G0/1 .1
.1 G0/0
Area 1
10.1.1.0/24
192.168.2.0/24
R1
R2
Notes: Media Description:
Create the media as indicated.

## Slide 81: Configuring Multiarea OSPF on R1
R1(config)# router ospf 10
R1(config-router)# router-id 1.1.1.1
R1(config-router)# network 10.1.1.1 0.0.0.0 area 1
R1(config-router)# network 10.1.2.1 0.0.0.0 area 1
R1(config-router)# network 192.168.10.1 0.0.0.0 area 0
R1(config-router)# end
R1#
Notes: Media Description:
Create the media as indicated.

## Slide 82: Configuring Multiarea OSPF on R2
R2(config)# router ospf 10
R2(config-router)# router-id 2.2.2.2
R2(config-router)# network 192.168.10.0 0.0.0.7 area 0
R2(config-router)# network 10.2.1.0 0.0.0.255 area 0
R2(config-router)# end
*Apr 19 18:11:04.029: %OSPF-5-ADJCHG: Process 10, Nbr 1.1.1.1 on Serial0/0/0 from LOADING to FULL, Loading Done
R2#
Notes: Media Description:
Create the media as indicated.

## Slide 83: Configuring Multiarea OSPF on R3
R3(config)# router ospf 10
R3(config-router)# router-id 3.3.3.3
R3(config-router)# network 192.168.10.6 0.0.0.3 area 0
R3(config-router)# network 192.168.1.1 0.0.0.0 area 2
R3(config-router)# network 192.168.2.1 0.0.0.0 area 2
R3(config-router)# end
*Apr 19 18:12:55.881: %OSPF-5-ADJCHG: Process 10, Nbr 2.2.2.2 on Serial0/0/1 from LOADING to FULL, Loading Done
R3#
Notes: Media Description:
Create the media as indicated.

## Slide 84: OSPFv3 Topology
Area 2
Area 0
Area 1
R3
:2 S0/0/1
R1
:1 S0/0/0
R2
:1 S0/0/1
G0/0 :1
:2 S0/0/0
G0/0 :1
G0/0 :1
2001:DB8:CAFE:A001::/64
2001:DB8:CAFE:3::/64
2001:DB8:CAFE:2::/64
2001:DB8:CAFE:1::/64
2001:DB8:CAFE:A002::/64
LLA: FE80::1
LLA: FE80::2
LLA: FE80::3
Notes: Media Description:
Create the media as indicated.

## Slide 85: Configuring Multiarea OSPFv3 on R1
R1(config)# ipv6 router ospf 10
R1(config-rtr)# router-id 1.1.1.1
R1(config-rtr)# exit
R1(config)# interface GigabitEthernet 0/0
R1(config-if)# ipv6 ospf 10 area 1
R1(config-if)# exit
R1(config)# interface Serial0/0/0
R1(config-if)# ipv6 ospf 10 area 0
*Apr 24 14:18:10.463: %OSPFv3-4-NORTRID: Process OSPFv3-10-IPv6 could not pick a router-id, please configure manually
Notes: Media Description:
Create the media as indicated.

## Slide 86: Configuring Multiarea OSPFv3 on R2
R2(config)# ipv6 router ospf 10
R2(config-rtr)# router-id 2.2.2.2
R2(config-rtr)# exit
R2(config)# interface g0/0
R2(config-if)# ipv6 ospf 10 area 0
R2(config-if)# interface s0/0/0
R2(config-if)# ipv6 ospf 10 area 0
R2(config-if)# interface s0/0/1
R2(config-if)# ipv6 ospf 10 area 0
Notes: Media Description:
Create the media as indicated.

## Slide 87: Configuring Multiarea OSPFv3 on R3
R3(config)# ipv6 router ospf 10
R3(config-rtr)# router-id 3.3.3.3
R3(config-rtr)# exit
R3(config)# interface g0/0
R3(config-if)# ipv6 ospf 10 area 2
R3(config-if)# interface s0/0/1
R3(config-if)# ipv6 ospf 10 area 0
R3(config-if)# end
Notes: Media Description:
Create the media as indicated.

## Slide 88: Configuring OSPF Route Summarization

## Slide 89: Why Summarize?
Summarization helps keep routing tables small.
Involves consolidating multiple routes into a single advertisement, which can then be propagated into the backbone area.
Summarized into type 3 LSAs, and sent to other areas.
  If area 1 had 30 networks to advertise, then 30 type 3 LSAs would be forwarded into the backbone.
  With route summarization, the ABR consolidates the 30 networks into one or a few advertisements.

## Slide 90: Propagating a Summary Route
Summarized
Type 3 LSA
Summarized
Type 3 LSA
Summarized
Type 3 LSA
Summarized
Type 3 LSA
Summarized
Type 3 LSA
Notes: Media Description:
Create the media as indicated.

## Slide 91: OSPF Route Summarization Topology
.225
Lo0
EIGRP
(172.16.0.0 /24
– 172.16.31.0/24)
.226
209.165.200.224/27
G0/1 .1
.1 G0/0
Area 2
192.168.1.0/24
Area 0
R3
S0/0/1 .6
.1 S0/0/0
S0/0/1 .5
10.2.1.0/24
G0/0 .1
10.1.2.0/24
192.168.10.0/30
192.168.10.4/30
.2 S0/0/0
G0/1 .1
.1 G0/0
Area 1
10.1.1.0/24
192.168.2.0/24
R1
R2
Notes: Media Description:
Create the media as indicated.

## Slide 92: Interarea Route Summarization
.225
Lo0
EIGRP
(172.16.0.0 /24
– 172.16.31.0/24)
.226
209.165.200.224/27
G0/1 .1
.1 G0/0
Area 2
192.168.1.0/24
Area 0
R3
S0/0/1 .6
.1 S0/0/0
S0/0/1 .5
10.2.1.0/24
G0/0 .1
10.1.2.0/24
192.168.10.0/30
192.168.10.4/30
.2 S0/0/0
G0/1 .1
.1 G0/0
Area 1
10.1.1.0/24
192.168.2.0/24
R1
R2
Summarize many routes into one LSA
Summarize many routes into one LSA
Notes: Media Description:
Create the media as indicated.

## Slide 93: External Route Summarization
.225
Lo0
EIGRP
(172.16.0.0 /24
– 172.16.31.0/24)
.226
209.165.200.224/27
G0/1 .1
.1 G0/0
Area 2
192.168.1.0/24
Area 0
R3
S0/0/1 .6
.1 S0/0/0
S0/0/1 .5
10.2.1.0/24
G0/0 .1
10.1.2.0/24
192.168.10.0/30
192.168.10.4/30
.2 S0/0/0
G0/1 .1
.1 G0/0
Area 1
10.1.1.0/24
192.168.2.0/24
R1
R2
Summarize external routes into one LSA
Summarize external routes into one LSA
Notes: Media Description:
Create the media as indicated.

## Slide 94: R1 Routing Table Before Summarization
R1# show ip route ospf | begin Gateway
Gateway of last resort is not set
10.0.0.0/8 is variably subnetted, 5 subnets, 2 masks
O 10.2.1.0/24 [110/648] via 192.168.10.2, 00:00:49, Serial0/0/0
O IA 192.168.1.0/24 [110/1295] via 192.168.10.2, 00:00:49, Serial0/0/0
O IA 192.168.2.0/24 [110/1295] via 192.168.10.2, 00:00:49, Serial0/0/0
192.168.10.0/24 is variably subnetted, 3 subnets, 2 masks
O 192.168.10.4/30 [110/1294] via 192.168.10.2, 00:00:49, Serial0/0/0
R1#
Notes: Media Description:
Create the media as indicated.

## Slide 95: R3 Routing Table Before Summarization
R3# show ip route ospf | begin Gateway
Gateway of last resort is not set
10.0.0.0/24 is subnetted, 3 subnets
O IA 10.1.1.0 [110/1295] via 192.168.10.5, 00:27:14, Serial0/0/1
O IA 10.1.2.0 [110/1295] via 192.168.10.5, 00:27:14, Serial0/0/1
O 10.2.1.0 [110/648] via 192.168.10.5, 00:27:57, Serial0/0/1
192.168.10.0/24 is variably subnetted, 3 subnets, 2 masks
O 192.168.10.0/30 [110/1294] via 192.168.10.5, 00:27:57, Serial0/0/1
R3#
Notes: Media Description:
Create the media as indicated.

## Slide 96: 3 Steps to Calculating the Summary Route
List the networks in binary format.
Count the number of far left matching bits to determine the mask for the summary route.
Copy the matching bits and then add zero bits to determine the summarized network address.
10.1.1.0 | 00001010.00000001.00000001.00000000
10.1.2.0 | 00001010.00000001.00000010.00000000
10.1.0.0 255.255.252.0 | 00001010.00000001.00000000.00000000 11111111.11111111.11111100.00000000
Step 1
First 22 bits match
Some bits are different
/22
10.1.0.0/22 or 10.1.0.0 255.255.252.000
Step 2
Step 3
Notes: Media Description:
Create the media as indicated.

## Slide 97: Summarizing Area 1 Routes on R1
R1(config)# router ospf 10
R1(config-router)# area 1 range 10.1.0.0 255.255.252.0
R1(config-router)#
Send summary route 10.1.0.0/22
Notes: Media Description:
Create the media as indicated.

## Slide 98: R1 Routing Table After Summarization
R1# show ip route ospf | begin Gateway
Gateway of last resort is not set
10.0.0.0/8 is variably subnetted, 6 subnets, 3 masks
O 10.1.0.0/22 is a summary, 00:00:09, Null0
O 10.2.1.0/24 [110/648] via 192.168.10.2, 00:00:09, Serial0/0/0
O IA 192.168.1.0/24 [110/1295] via 192.168.10.2, 00:00:09, Serial0/0/0
O IA 192.168.2.0/24 [110/1295] via 192.168.10.2, 00:00:09, Serial0/0/0
192.168.10.0/24 is variably subnetted, 3 subnets, 2 masks
O 192.168.10.4/30 [110/1294] via 192.168.10.2, 00:00:09, Serial0/0/0
R1#
Notes: Media Description:
Create the media as indicated.

## Slide 99: R3 Routing Table After Summarization
R3# show ip route ospf | begin Gateway
Gateway of last resort is not set
10.0.0.0/8 is variably subnetted, 2 subnets, 2 masks
O IA 10.1.0.0/22 [110/1295] via 192.168.10.5, 00:00:06, Serial0/0/1
O 10.2.1.0/24 [110/648] via 192.168.10.5, 00:29:23, Serial0/0/1
192.168.10.0/24 is variably subnetted, 3 subnets, 2 masks
O 192.168.10.0/30 [110/1294] via 192.168.10.5, 00:29:23, Serial0/0/1
R3#
Notes: Media Description:
Create the media as indicated.

## Slide 100: Summarizing Area 2 Routes on R3
R3(config)# router ospf 10
R3(config-router)# area 2 range 192.168.0.0 255.255.252.0
R3(config-router)# end
SHOW R1’s routing table
Send summary route 192.168.0.0 /22
Notes: Media Description:
Create the media as indicated.

## Slide 101: Verifying OSPF Status on R1
R1# show ip protocols
*** IP Routing is NSF aware ***
Routing Protocol is "ospf 10"
Outgoing update filter list for all interfaces is not set
Incoming update filter list for all interfaces is not set
Router ID 1.1.1.1
It is an area border router
Number of areas in this router is 2. 2 normal 0 stub 0 nssa
Maximum path: 4
Routing for Networks:
10.1.1.1 0.0.0.0 area 1
10.1.2.1 0.0.0.0 area 1
192.168.10.1 0.0.0.0 area 0
Routing Information Sources:
Gateway Distance Last Update
3.3.3.3 110 02:20:36
2.2.2.2 110 02:20:39
Distance: (default is 110)
R1#
Notes: Media Description:
Create the media as indicated.

## Slide 102: Verifying OSPF Enabled Interface on R1
R1# show ip ospf interface brief
Interface PID Area IP Address/Mask Cost State Nbrs F/C
Se0/0/0 10 0 192.168.10.1/30 64 P2P 1/1
Gi0/1 10 1 10.1.2.1/24 1 DR 0/0
Gi0/0 10 1 10.1.1.1/24 1 DR 0/0
R1#
Notes: Media Description:
Create the media as indicated.

## Slide 103: Verifying OSPF Routes on R1
R1# show ip route ospf | begin Gateway
Gateway of last resort is not set
10.0.0.0/8 is variably subnetted, 5 subnets, 2 masks
O 10.2.1.0/24 [110/648] via 192.168.10.2, 00:26:03, Serial0/0/0
O IA 192.168.1.0/24 [110/1295] via 192.168.10.2, 00:26:03, Serial0/0/0
O IA 192.168.2.0/24 [110/1295] via 192.168.10.2, 00:26:03, Serial0/0/0
192.168.10.0/24 is variably subnetted, 3 subnets, 2 masks
O 192.168.10.4/30 [110/1294] via 192.168.10.2, 00:26:03, Serial0/0/0
R1#
Notes: Media Description:
Create the media as indicated.

## Slide 104: CIS 185 CCNP ROUTE Chapter 3: Implementing OSPF Part 1
Rick Graziani
Cabrillo College
graziani@cabrillo.edu